## Slide 1
NEUROLINK / BIOLOGY FOR ENGINEERS
NeuroLink
An educational brain–computer interface simulator
Team 2 · CE-SE-A | Synthetic signals only · Not a medical device
01
From a noisy waveform
to an artificial command
Generate → Filter → Extract → Classify → Visualize
EXPERIENTIAL LEARNING
Team No. 2
Class: CE-SE-A
Biology for Engineers
Educational prototype using simulated EEG-like signals — not live brain data.
Notes: Presenter: Aditya Dugar
Introduce Team 2 and the Biology for Engineers experiential-learning project. Explain that the goal is to learn the software stages of a BCI without a headset. Say clearly that all displayed signals are generated and that left/right are artificial labels. The presentation moves from biology to the processing pipeline, a demonstration, and the limits of what the result proves.

## Slide 2
NEUROLINK / BIOLOGY FOR ENGINEERS
Team 2 · contribution & presentation plan
Assigned responsibilities for preparation, explanation and demonstration
Team 2 · CE-SE-A | Synthetic signals only · Not a medical device
02
MEMBER
STUDENT ID
RESPONSIBILITY
SLIDES
Aditya Dugar
25BRTSN003
Biology, motivation & introduction
1, 3–4
Kushal Chaudhary
25BTRSN025
Acquisition concepts & synthetic signals
5–6
Prince Jatheen Rout
25BTRSN034
Filtering, artifacts & scientific limits
7, 14
Raunak Bothra
25BTRSN037
Features & machine-learning pipeline
8–9
Vijaya Rupesh N
25BTRSN053
Validation, dashboard & live demo
10–12
Yashas L Rao
25BTRSN055
Assistive-tech case study & learning review
13, 15–16
Shared: integration review, rehearsal and questions. Roles are a proposed allocation, not verified individual authorship.
Notes: Presenter: All members
These are assigned responsibilities, not a historical authorship claim. Each member should understand their module, rehearse the explanation, and review the associated code or evidence. Aditya frames the biology; Kushal explains signals; Prince covers filtering and limitations; Raunak covers features and learning; Vijaya demonstrates and validates; Yashas connects the case study and learning outcomes. Use this table to organize rehearsal.

## Slide 3
NEUROLINK / BIOLOGY FOR ENGINEERS
The learning challenge
How does a waveform become a usable command?
Team 2 · CE-SE-A | Synthetic signals only · Not a medical device
03
Observe
Compare raw and filtered signals using the same time axis.
Measure
Extract two named frequency-band features from each example.
Interpret
Classify generated patterns and explain what the output can—and cannot—mean.
Learning objective: explain each transformation, then test its behavior.
Notes: Presenter: Aditya Dugar
Our learning question is how a noisy time-domain signal becomes a compact representation and a command. Real acquisition would require equipment and experimental controls beyond this prototype. A simulator makes the stages observable and repeatable. Explain success in terms of an understandable pipeline, reproducibility and honest boundaries, not a clinical performance target.

## Slide 4
NEUROLINK / BIOLOGY FOR ENGINEERS
Biology first: what a BCI measures
Neural activity → measurement → signal processing → external output
Team 2 · CE-SE-A | Synthetic signals only · Not a medical device
04
Real EEG pathway
Electrodes record voltage differences.
Signals vary across people and sessions.
Eye, muscle and motion activity can affect recordings.
Our educational substitution
Python generates a waveform.
Amplitude uses arbitrary units.
No headset, human participant or recorded EEG is involved.
Notes: Presenter: Aditya Dugar
A real BCI measures neural activity and maps selected patterns to an output. EEG measures electrical potential differences through electrodes; it is affected by the recording setup and unwanted signal contributions. Our app does not perform that acquisition step. Make the distinction before showing any waveform so the audience does not mistake synthetic sinusoids for recordings. Hand over to Kushal to explain how the simulation replaces acquisition.

## Slide 5
NEUROLINK / BIOLOGY FOR ENGINEERS
The complete software pipeline
Team 2 · CE-SE-A | Synthetic signals only · Not a medical device
05
01
Generate
512 samples
02
Filter
1–40 Hz
03
Extract
2 features
04
Classify
left / right
05
Display
plots + cursor
NumPy · SciPy · scikit-learn · joblib · Streamlit · Plotly
Python 3.12 · Local-first application with an optional Streamlit-hosted demo
Notes: Presenter: Kushal Chaudhary
Walk from left to right through the pipeline. Every example uses 512 samples. Filtering returns the same number of samples; feature extraction reduces that waveform to two numbers. The trained classifier maps those numbers to an artificial category. The Streamlit dashboard shows the intermediate evidence rather than hiding it behind a final label. Name NumPy, SciPy and scikit-learn as implementation tools, without treating a software library as biological validation.

## Slide 6
NEUROLINK / BIOLOGY FOR ENGINEERS
Create two deliberately distinct patterns
Actual generated examples · seed 7 · arbitrary amplitudes
Team 2 · CE-SE-A | Synthetic signals only · Not a medical device
06
Chart: Time (seconds)
256 Hz
2 seconds
512 samples
left: emphasizes 8 Hz
right: emphasizes 22 Hz
Noise + drift + interference
Left and right describe generator settings, not a person’s intention.
Notes: Presenter: Kushal Chaudhary
These native charts contain actual outputs from generate_eeg using seed 7, not stock EEG images. Left emphasizes 8 Hz and right 22 Hz. The generator adds a weaker alternate component, 0.3 Hz drift, 60 Hz interference and Gaussian noise with randomized phase and amplitude. At 256 samples per second for two seconds, the output has 512 samples. Explain that the deliberately different patterns make classification easy; a fixed seed makes the example repeatable.

## Slide 7
NEUROLINK / BIOLOGY FOR ENGINEERS
Filter the signal, not every artifact
Butterworth band-pass · second-order sections · offline zero phase
Team 2 · CE-SE-A | Synthetic signals only · Not a medical device
07
Chart: Time (seconds)
Pass band
1–40 Hz
Same sample count
Finite output checked
Future samples required
Edge effects remain
Motion, eye and muscle artifacts may overlap the passed frequencies.
Notes: Presenter: Prince Jatheen Rout
The chart compares the actual raw and filtered left example at seed 7. Explain the fourth-order Butterworth band-pass, represented as second-order sections. The algorithm runs forward and backward to produce zero-phase output. This uses future samples and therefore is an offline demonstration. Filtering attenuates out-of-band content but cannot distinguish an artifact inside the useful band from desired content. Edge effects are also possible in this short window.

## Slide 8
NEUROLINK / BIOLOGY FOR ENGINEERS
Reduce 512 samples to two features
Center → real FFT → squared normalized magnitude → band averages
Team 2 · CE-SE-A | Synthetic signals only · Not a medical device
08
Chart: Mean power (arbitrary units²)
| 1 ≤ f < 12 Hz | 12 ≤ f ≤ 40 Hz
left | 0.031302 | 0.0011796
right | 0.0029864 | 0.011563
Stable feature names
mean_power_1_12_hz
mean_power_12_40_hz
Mean |rFFT(x − mean(x)) / N|²
within each band
The 12 Hz bin is counted once. Empty bands raise an explicit error.
Notes: Presenter: Raunak Bothra
First subtract the mean, then calculate the real FFT. For each positive-frequency bin, square the magnitude normalized by the sample count. Average those values in each band. We choose a nonoverlapping convention: 1 inclusive to 12 exclusive, then 12 through 40 inclusive. These are mean powers per FFT bin, not integrated power or a PSD. The chart uses actual processed seed-7 examples. Explain that the relative power distribution gives the classifier useful separation.

## Slide 9
NEUROLINK / BIOLOGY FOR ENGINEERS
Train a reproducible classifier
Balanced synthetic data · fixed random state · held-out evaluation
Team 2 · CE-SE-A | Synthetic signals only · Not a medical device
09
400 examples
200 left + 200 right
Independent example seeds
One generator family
300 / 100 split
Stratified 75% / 25%
Fit scaler on training only
Hold test examples aside
Model pipeline
StandardScaler
LogisticRegression
Save/load with joblib
Reproducibility supports teaching; it does not establish real EEG generalization.
Notes: Presenter: Raunak Bothra
The dataset has 200 examples in each class. A fixed-seed stratified split preserves balance: 300 examples for training and 100 for testing. StandardScaler is fitted on the training split only, preventing test statistics from entering training. Logistic regression learns the separation between the two synthetic feature patterns. A local joblib artifact can be loaded later; on a fresh hosted deployment the dashboard can build a cached in-memory synthetic model. Probabilities remain model outputs, not confidence about human intent.

## Slide 10
NEUROLINK / BIOLOGY FOR ENGINEERS
Validation: what the results demonstrate
Source: saved synthetic metrics and locally executed automated tests
Team 2 · CE-SE-A | Synthetic signals only · Not a medical device
10
100 / 100
held-out synthetic examples correct
Confusion matrix
Actual → predicted
left
right
left
50
0
right
0
50
58 tests passed locally*
Synthetic accuracy is NOT evidence of real EEG decoding or clinical effectiveness.
*See presenter guide for the verification date and command.
Notes: Presenter: Vijaya Rupesh N
The saved seed-42 training report contains 100 test examples: 50 per class, all correctly classified. Report the 100% figure only with the synthetic-only qualification. These classes were designed to be different, so this is not comparable to a clinical BCI result. Automated tests cover parameter validation, signal determinism, filter behavior, FFT band boundaries, dataset balance, saved models, dashboard interactions, model fallback and cursor bounds. Cite the actual local test run reported in the presenter guide.

## Slide 11
NEUROLINK / BIOLOGY FOR ENGINEERS
An interactive dashboard makes the stages visible
Interface map · representative values from the actual seed-7 left example
Team 2 · CE-SE-A | Synthetic signals only · Not a medical device
11
INPUT
Artificial class: left
Seed: 7
Generate and process
Optional simulated cursor
Raw + filtered waveform comparison
Low-band feature: 0.0313
High-band feature: 0.0012
Prediction: left
Model score: 0.9855
Zoomable chart · explicit errors · scientific explanation
Interface schematic; model scores do not measure actual human intention.
Notes: Presenter: Vijaya Rupesh N
This slide is a schematic of the implemented dashboard, not a screenshot. The sidebar selects the artificial class, reproducible seed and optional cursor. The output contains a Plotly raw/filtered chart, named feature values, prediction and class scores. The displayed result retains its original seed and label until processed again. Missing local model files trigger cached in-memory synthetic training; other failures are shown as actionable errors. The synthetic-data notice is always included in the app.

## Slide 12
NEUROLINK / BIOLOGY FOR ENGINEERS
Live demonstration · about 90 seconds
Show the causal chain rather than only the final label
Team 2 · CE-SE-A | Synthetic signals only · Not a medical device
12
01
Choose left · seed 7
Compare raw/filtered traces and inspect the low-band feature.
02
Choose right · seed 7
Compare the feature balance and predicted artificial label.
03
Enable cursor · reset to 50
Left → 40; then right → 50. Bounds are 0–100.
Local backup: python -m streamlit run app.py
Notes: Presenter: Vijaya Rupesh N
Before presenting, open the local dashboard or the working Streamlit deployment. Start at seed 7 with the cursor disabled. Generate left and point out the slower dominant oscillation and larger low-band feature. Generate right and compare the faster oscillation and higher upper-band feature. Enable the cursor and reset to 50: process left once for 40, then right once for 50. Changing controls alone should not move the cursor. If the network is unavailable, run locally using the command on this slide; the preceding charts provide a backup.

## Slide 13
NEUROLINK / BIOLOGY FOR ENGINEERS
Real assistive technology: the BrainGate study
A separate published research example — not a capability of our simulator
Team 2 · CE-SE-A | Synthetic signals only · Not a medical device
13
Published research
Two participants with tetraplegia
Implanted motor-cortex electrodes
Robotic reaching and grasping
NeuroLink
Generated sinusoidal patterns
Two FFT features and an artificial label
On-screen cursor simulation
Hochberg et al., Nature 485, 372–375 (2012) · doi:10.1038/nature11076
Notes: Presenter: Yashas L Rao
Keep this case study clearly separate from NeuroLink. Hochberg and colleagues reported in 2012 that two participants with tetraplegia controlled robotic reaching and grasping using implanted motor-cortex electrode arrays. This was an investigational intracortical neural-interface study, not scalp EEG. It illustrates the motivation for assistive BCI work but does not validate our classifier or simulator. Do not generalize a two-participant research demonstration to universal effectiveness. Source: https://pmc.ncbi.nlm.nih.gov/articles/PMC3640850/

## Slide 14
NEUROLINK / BIOLOGY FOR ENGINEERS
Scientific boundaries we must keep visible
What works in this simulator does not establish what works on a person
Team 2 · CE-SE-A | Synthetic signals only · Not a medical device
14
Data boundary
Synthetic only
Arbitrary amplitudes
Artificial labels
Method boundary
Offline zero phase
Incomplete artifact removal
Pedagogical band choices
Evidence boundary
Same generator family
No human-intent confidence
No clinical validation
Real EEG is future work requiring a separate dataset, protocol and evaluation.
Notes: Presenter: Prince Jatheen Rout
Use this slide to prevent overclaiming during questions. We have no measured neural signal, no verified motor-imagery label and no clinical validation. Filtering is not complete artifact removal and zero-phase filtering is not streaming. Synthetic train and test samples come from the same generator family. A future real-EEG project would require a documented licensed dataset, careful leakage controls such as subject/session separation as appropriate, and evaluation on genuinely held-out data. It would be a separate study.

## Slide 15
NEUROLINK / BIOLOGY FOR ENGINEERS
Experiential learning: build, observe, explain
Connect biology concepts to engineering decisions
Team 2 · CE-SE-A | Synthetic signals only · Not a medical device
15
Build & inspect
Modular signal processing
Reproducible experiments
Visible intermediate outputs
Test & question
Check shape and finite values
Test frequency behavior
Challenge accuracy claims
Explain & reflect
Identify artifacts
Explain synthetic data
State scientific limits
Discussion: why can 100% synthetic accuracy still tell us very little about real EEG?
Notes: Presenter: Yashas L Rao
Frame these as learning takeaways and a reflection plan rather than invented student testimonials. Each member should be able to explain a transformation using evidence from the app. Ask the team what changes when seed changes, why a filter cannot remove every artifact, and why a high test score can be misleading. Close by restating that the outcome is a working and testable educational signal-processing pipeline. Invite questions on either the engineering implementation or the distinction from real BCI research.

## Slide 16
NEUROLINK / BIOLOGY FOR ENGINEERS
References & project resources
Team 2 · CE-SE-A | Synthetic signals only · Not a medical device
16
Primary research
Hochberg et al. (2012). Reach and grasp by people with tetraplegia using a neurally controlled robotic arm. Nature 485, 372–375.
https://pmc.ncbi.nlm.nih.gov/articles/PMC3640850/
Project repository
Source code, README, specifications and setup instructions.
https://github.com/CoBrIX44/neurolink-bci-simulator
Methods & evidence
PRD.md · docs/SCIENCE_AND_USER_GUIDE.md · docs/IMPLEMENTATION_NOTES.md · models/neurolink.metrics.json
Software documentation
SciPy signal filtering · scikit-learn pipelines · Streamlit application framework
https://docs.scipy.org/doc/scipy/reference/signal.html
Notes: Presenter: Yashas L Rao / all members
Use the repository and local documentation for implementation-specific statements, and the cited primary research for the assistive case study. The class should not treat framework documentation as evidence of biological efficacy. The app deployment was reported successful by the team during setup; the deck does not claim an independent cloud availability test. Confirm the current hosted link from the repository About section before the presentation. Thank the audience and invite questions.